## Slide 1: Data Collection and Analysis Area Measurement
How to measure the perimeter and area of an arbitrary closed shape?

## Slide 2: Data Collection and Analysis Area Measurement
How to measure the perimeter and area of an arbitrary closed shape?
Consider Descartes’ method:
Could we do this by driving a robot around the shape?
From Historical Connections in Mathematics, Volume III, Area the Easy Way
INSTRUCTIONS
Beginning with any vertex, list the coordinates of the vertices in order, moving counter-clockwise around the polygon. List the first pair again at the end. Find the diagonal products from left to right. Find the diagonal products from right to left. Sum each column of products. Find their difference and divide by 2. This is the polygon’s area.

## Slide 3: Data Collection and Analysis Area Measurement
Need to generate (x, y) pairs as the robot follows the line around…
But unlike the plotted curve, the robot does not know what the next pair will be.
Need to find a way to remember the last point and calculate the next one.
Just a little trigonometry…
and a compass.
Inspired by Area the Easy Way
(X old, Y old)
North
Distance
(X new, Y new)
Heading
ΔX
ΔY
X new = X old + ΔX
Y new = Y old + ΔY
ΔX = Dist *Sine (Hdg)
ΔY = Dist *Cosine (Hdg)

## Slide 4: Data Collection and Analysis Area Measurement
Need to generate (x, y) pairs as the robot follows the line around…
But unlike the plotted curve, the robot does not know what the next pair will be.
Need to find a way to remember the last point and calculate the next one.
Just a little trigonometry…
and a compass.
Inspired by Area the Easy Way
(X new, Y new)
Distance
(X old, Y old)
North
Heading
ΔX
ΔY
X new = X old + ΔX
Y new = Y old + ΔY
ΔX = Dist *Sine (Hdg)
ΔY = Dist *Cosine (Hdg)
Sine and cosine provide positive and negative factors that scale the sides of the right triangle.

## Slide 5: Data Collection and Analysis Area Measurement
Show development of the path as the robot follows along the orange curve.
Inspired by Area the Easy Way
X new = X old + ΔX
Y new = Y old + ΔY
ΔX = Dist *Sine (Hdg)
ΔY = Dist *Cosine (Hdg)
Sine and cosine provide positive and negative factors that scale the sides of the right triangle.

## Slide 6: Data Collection and Analysis Area Measurement
Show development of the path as the robot follows along the orange curve.
Inspired by Area the Easy Way
X new = X old + ΔX
Y new = Y old + ΔY
ΔX = Dist *Sine (Hdg)
ΔY = Dist *Cosine (Hdg)
Sine and cosine provide positive and negative factors that scale the sides of the right triangle.
ΔX
ΔY

## Slide 7: Data Collection and Analysis Area Measurement
(X1, Y1)
(X0, Y0)
North
ΔX
ΔY
(X2, Y2)
Example path showing generated (x, y) pairs as the robot follows the line around.
Inspired by Area the Easy Way
X new = X old + ΔX
Y new = Y old + ΔY
ΔX = Dist *Sine (Hdg)
ΔY = Dist *Cosine (Hdg)
Sine and cosine provide positive and negative factors that scale the sides of the right triangle.

## Slide 8: Data Collection and Analysis Area Measurement
(X1, Y1)
(X0, Y0)
North
ΔX
ΔY
(X2, Y2)
(X3, Y3)
(X4, Y4)
(X5, Y5)
Example path showing generated (x, y) pairs as the robot follows the line around.
Inspired by Area the Easy Way
X new = X old + ΔX
Y new = Y old + ΔY
ΔX = Dist *Sine (Hdg)
ΔY = Dist *Cosine (Hdg)
Sine and cosine provide positive and negative factors that scale the sides of the right triangle.

## Slide 9: Data Collection and Analysis Area Measurement – two plots
Circle with Distance = 1 inch
Inspired by Area the Easy Way
(X old, Y old)
North
Distance
(X new, Y new)
Heading
ΔX
ΔY
X new = X old + ΔX
Y new = Y old + ΔY
ΔX = Dist *Sine (Hdg)
ΔY = Dist *Cosine (Hdg)
Rectangle with Distance = 1 inch

## Slide 10: Data Collection and Analysis Area Measurement – two plots
Circle with Distance = 1 inch
Inspired by Area the Easy Way
Rectangle with Distance = 1 inch
Red arrows indicate error accumulated through each run.

## Slide 11: Data Collection and Analysis Area Measurement